## Slide 1: VSM representation by classes
Physical and logical objects of the VSM setup
Measurement
Analog
In/Out
Filtering Data
File
(measured data)
Hysteresis
Magnet
Configuration

## Slide 2: Hardware <–> Code
AnalogIO
class
ADC
DAC
Pickup 1
Pickup 2
Hall probe
Power supply (magnet)

## Slide 3: VSM representation by classes
logical connection
Analog
In/Out
Filtering Data
Magnet
Door to the „real“ world
Uses a MagField and DataFilter object to do its job
Transforms magn. field [Oe] to output voltage (in order to control the magnets power supply)
Transforms hall probe voltage to magn. Field
Knows all the mathematics for this
Different filter types, which reduce
outliers and average data points
Configuration
Program configuration/parameters

## Slide 4: VSM representation by classes
logical connection
Analog
In/Out
Analog In
(mcc)
Analog Out
(mcc)
AnalogIn/Out inherits (all properties and methods) from both:
Analog In and Analog Out which contain the code
for controlling MCC hardware
Analog
In/Out
Analog In
(digilent)
Analog Out
(mcc)
Base classes
(superclasses)
When changing analog hardware:
Base classes can be exchanged (assuming they have the same structure)
The other parts of the Program will not recognize this exchange
children
(subclasses)

## Slide 5: VSM representation by classes
logical connection (measurement initialization)
Measurement
Analog
In/Out
Filtering Data
File
(measured data)
Hysteresis
Magnet
Measure hysteresis loop
Ana_IO
- data_filter
- magn_field
DataFile
create
create
create
(median filter)
create
HystLoop
create